## Slide 1: Data conversion – binary to text format (FL30)
Work through example on
https://renkulab.io/p/eric.pohl/discharge-calculation-dilution-method
In RStudio on renkulab.io (same workflow on your own computer)

## Slide 2
On the SD-card of the fluorometer are 3 files
cal.dat
Calibrat.dat
fXXXX.txt (XXXX is the serial number of the logger)
I call each year’s file according to the
Year, e.g. 2022
Logger number, e.g. f1664
“2022 - f1664.txt”
The files need to be converted …

## Slide 3
Before conversion
(binary format)
After conversion

## Slide 4
https://renkulab.io/p/eric.pohl/discharge-calculation-dilution-method
Takes around 2 minutes to open
click

## Slide 5
click
Opening the program. Directory: work/CA-hydroworkshop/materials/Fluorometer/KG_G354/R/003_Qcalc.R

## Slide 6
Click, click, click …
1
2
3
4
5
Opening the program. Directory: work/CA-hydroworkshop/materials/Fluorometer/KG_G354/R/001_prep….R

## Slide 7
This is the conversion “script” (program)

## Slide 8
This is the conversion “script” (program)
That’s it. You don’t need to change anything else!
The program is designed that you only have to change very few things!
These things are:
Define the input name
Define the output name

## Slide 9
Scroll down to where it says:
“# ------------ NO NEED TO CHANGE ANYTHING HEREAFTER --------------- #
Click into this line
Run line by line [Ctrl]+[Enter]
You will see graphs produced
It will write the mV output file

## Slide 10
Possible issues
Corrupt file from the FL30
   Error when running the script/program
  Solution:
    Read error message
    It will say where in the original file the error occurs
    Remove the line
    Try again
Switched interval (e.g. from 2 seconds to 30 seconds)
   Error when running the script/program
  Solution:
    Cut out (delete) the part; this part will look different in the original file
Prepare the original input file:
  Check the dates and remove all lines that are not from the measuring period
  Some loggers have a wrong date (usually maximum a few days off)
  Start from the last entry (check with your filed notebook when the last measurement was made)
  Identify the date and time offset
  Use that information to remove non-relevant data entries